## Slide 1: Multi-Mode alu with Interrupt Support

## Slide 2: AGENDA
Design Requirements ​
Verification Plan
Environment Architecture
Makefile
Simulation Results on VCS
​Coverage Plan on Verdi
Resources

## Slide 3: Design Requirements

## Slide 4: Design Requirements

## Slide 5: Design Requirements
ID | Signal | Description
DR1 | alu_clk | Frequency is 32 MHz (31 nanoseconds 1000/32) Positive edge triggered clock.

## Slide 6: Design Requirements
ID | Signal | Description
DR2 | rst_n | Active low, asynchronous reset. Whenever rst_n is low, then alu_out and alu_irq should be driven to 0. rst_n should be asserted at least once at start-up.

## Slide 7: Design Requirements
ID | Signal | Description
DR3 | alu_in_a | Synchronized to alu_clk, positive edge trigger. When alu_op_a == NAND , alu_enable == 1, alu_enable_a == 1 and alu_enable_b == 0 then alu_in_a can’t take value of 8’hff. When alu_op_b == NOR, alu_enable == 1, alu_enable_a == 0 and alu_enable_b == 1 then alu_in_a can’t take a value of 8’hf5.

## Slide 8: Design Requirements
ID | Signal | Description
DR4 | alu_in_b | Synchronized to alu_clk, positive edge trigger. When alu_op_a == AND, alu_enable == 1, alu_enable_a == 1 and alu_enable_b == 0 then alu_in_b can’t take value of 8’h0. When alu_op_a == NAND, alu_enable == 1, alu_enable_a == 1 and alu_enable_b == 0 then alu_in_b can’t take value of 8’h03. When alu_op_a == AND, alu_enable == 1, alu_enable_a == 0 and alu_enable_b == 1 then alu_in_b can’t take value of 8’h03.

## Slide 9: Design Requirements
ID | Signal | Description
DR5 | alu_enable | Synchronized to alu_clk, positive edge trigger. If alu_enable is de-asserted: All outputs should be maintained, if rst_n is high, regardless of alu_enable_a or alu_enable_b. If alu_enable is asserted: alu_enable_a and alu_enable_b can’t be asserted at the same time.

## Slide 10: Design Requirements
ID | Signal | Description
DR6 | alu_enable_a alu_enable_b | Synchronized to alu_clk, positive edge trigger. When alu_enable is asserted: if alu_enable_a == 0 and alu_enable_b == 0, it is legal and all outputs should be maintained. if alu_enable_a == 0 and alu_enable_b == 1, it is legal and the ALU should do operation b. if alu_enable_a == 1 and alu_enable_b == 0, it is legal and the ALU should do operation a. if alu_enable_a == 1 and alu_enable_b == 1, it is illegal and the output depends on RTL that cover this case. (Note: RTL can have //full case Synopsys so this case will be excluded.)

## Slide 11: Design Requirements
ID | Signal | Description
DR7 | alu_op_a | Synchronized to alu_clk, positive edge trigger. When it is 2’b00, alu_out should be the AND-ing of the inputs. When it is 2’b01, alu_out should be the NAND-ing of the inputs. When it is 2’b10, alu_out should be the OR-ing of the inputs. When it is 2’b11, alu_out should be the XOR-ing of the inputs. (Note: The design may don’t have a default case, all cases are covered)

## Slide 12: Design Requirements
ID | Signal | Description
DR8 | alu_op_b | Synchronized to alu_clk, positive edge trigger. When it is 2’b00, alu_out should be the XNOR-ing of the inputs. When it is 2’b01, alu_out should be the AND-ing of the inputs. When it is 2’b10, alu_out should be the NOR-ing of the inputs. When it is 2’b11, alu_out should be the OR-ing of the inputs. (Note: The design may don’t have a default case, all cases are covered)

## Slide 13: Design Requirements
ID | Signal | Description
DR9 | alu_irq_clr | Synchronized to alu_clk, positive edge trigger. It should be high for at least one clock cycle then it gets de-asserted. It should be high after at least one clock cycle from the assertion of alu_irq. It is an active high clear signal.

## Slide 14: Design Requirements
ID | Signal | Description
DR10 | alu_out | Synchronized to alu_clk, positive edge trigger. Should be as expected, according to the given table, after one clock cycle from applying the inputs. If alu_enable and alu_enable_a are asserted, and alu_enable b is de-asserted while alu_op_a is NAND then alu_out never be 8’h00, due to the constrain on alu_in_a.

## Slide 15: Design Requirements
ID | Signal | Description
DR11 | alu_irq | Synchronized to alu_clk, positive edge trigger. It should be asserted after one clock cycle from the event that triggers it. Events that assert it to high, in case of other events alu_irq maintains its value.

## Slide 16: Design Requirements
ID | Signal | Description
DR11 | alu_irq | When alu_enable && alu_enable_a && !alu_enable b, operation a: If alu_op_a is AND, alu_in_a is 8’hFF and alu_in_b is 8’hFF. If alu_op_a is NAND and ~(in_a & in b) equals 8’h00. (Note: this case can’t happen) If alu_op_a is OR and (alu_in_a ¦ alu_in_b) equals 8’hE8. If alu_op_a is XOR and (alu_in_a ^ alu_in_b) equals 8’h83.

## Slide 17: Design Requirements
ID | Signal | Description
DR11 | alu_irq | When alu_enable && alu_enable_b && !alu_enable a, operation b: If alu_op_b is XNOR and (alu_in_a ~^ alu_in_b ) equals 8’hF1. If alu_op_b is AND and (alu_in_a & alu_in b) equals 8’hF4. If alu_op_b is NOR and ~(alu_in_a ¦ alu_in_b) equals 8’hF5. If alu_op_b is OR and (alu_in_a ¦ alu_in_b) equals 8’hFF.

## Slide 18: Design Requirements
ID | Signal | Description
DR11 | alu_irq | It should be high until alu_irq_clr is asserted. It should be de-asserted after one clock cycle from asserting alu_irq_clr. Event has a priority over alu_irq_clr, when there is an event from the previous ones and alu_irq_clr is asserted at that time, then alu_irq should be high.

## Slide 19: Verification Plan

## Slide 20: Verification Plan
ID | Signal | Description
VR1 | alu_clk | Driven positive edge trigger clock with a period of 31.25 ns, (1000/32MHz). (Note: timescale 1ns/1ps)

## Slide 21: Verification Plan
ID | Signal | Description
VR2 | rst_n | Drive it with 0 at the start, then it can be 0 or 1 at different times during normal operation independent of the clock, most of the time it is high. Cover that reset is de-asserted and asserted. Check that outputs are driven to all 0’s immediately when it is low. Check that outputs are as expected when it is high.

## Slide 22: Verification Plan
ID | Signal | Description
VR3 | alu_in_a | Driven constrained randomly. Cover that the forbidden values aren’t generated. Cover that all input pins toggle from 1 to 0 and vice versa.

## Slide 23: Verification Plan
ID | Signal | Description
VR4 | alu_in_b | Driven constrained randomly. Cover that the forbidden values are not generated. Cover that all input pins toggle from 1 to 0 and vice versa.

## Slide 24: Verification Plan
ID | Signal | Description
VR5 | alu_enable | Drive it with 1 or 0, most of the time it is high. Cover that alu_enable, alu_enable_a and alu_enable_b toggle from 1 to 0 and vice versa Check that all outputs are maintained when alu_enable is low.

## Slide 25: Verification Plan
ID | Signal | Description
VR6 | alu_enable_a | Drive it with 1 or 0, most of the time alu_enable_a dosen’t equal alu_enable_b. Cover that alu_enable_a toggles with all variations of alu_enable. Check that when alu_enable_a is high, alu_out is generated according to operation a.

## Slide 26: Verification Plan
ID | Signal | Description
VR7 | alu_enable_b | Drive it with 1 or 0, most of the time alu_enable_a dosen’t equal alu_enable_b. Cover that alu_enable_b toggles with all variations of alu_enable. Check that when alu_enable_b is high, alu_out is generated according to operation b

## Slide 27: Verification Plan
ID | Signal | Description
VR7 | alu_op_a | Driven with all possible combinations randomly. Cover all possible combinations while alu_enable and alu_enable_a are high, and cover all other possible cases, listed in design requirements. Check that when the operation is NAND while alu_enable and alu_enable_a are asserted to high, alu_out will never be 8’h00.

## Slide 28: Verification Plan
ID | Signal | Description
VR8 | alu_op_b | Driven with all possible combinations randomly. Cover all possible combinations while alu_enable and alu_enable_b are high, and cover all other possible cases, listed in design requirements.

## Slide 29: Verification Plan
ID | Signal | Description
VR9 | alu_irq_clr | Drive it with 1 while alu_irq is de-asserted. Cover alu_irq_clr that is asserted and alu_irq is de-asserted. Check if alu_irq is still 0 or not. Drive it with 1 after alu_irq is asserted. Cover that alu_irq_clr is asserted and alu_irq is also asserted. Check that alu_irq is cleared, equals 0. Drive it with 0 regardless of the value of alu_irq, 1 or 0. Cover that alu_irq_clr is low when alu_irq is asserted and de-asserted at different times. Check that alu_irq is maintained.

## Slide 30: Verification Plan
ID | Signal | Description
VR10 | alu_out | Cover that all alu_out combinations that asserts alu_irq are generated. Cover that alu_out pins toggles. Check that alu_out is asserted after one clock cycle from applying the inputs. Check that alu_out is maintained when alu_enable_a and alu_enable_b are asserted to low at the same time.

## Slide 31: Verification Plan
ID | Signal | Description
VR11 | alu_irq | Check that alu_irq is asserted to high at the same cycle as alu_out. Check that alu_irq isn’t asserted unless alu_out is one of the cases listed in the design requirements. Drive alu_irq_clr to high while there are two successive events that assert alu_irq.

## Slide 32: Verification Plan
ID | Signal | Description
VR11 | alu_irq | Cover that alu_irq_clr is asserted while there is two successive events that assert alu_irq. Check that events have priority over alu_irq_clr Check that alu_irq is low when alu_irq_clr high, taking into consideration that there isn’t two successive events. Check that alu_irq is still asserted when there is two successive events while alu_irq_clr is high. Check that alu_irq is de-asserted after one clock cycle from the assertion of alu_irq_clr.

## Slide 33: Environment Architecture

## Slide 34: Environment Architecture
Black box

## Slide 35: Environment Architecture

## Slide 36: Makefile

## Slide 37: Makefile
#--------------------------------------------
comp : clean vcs coverage_html cov_verdi
#---------------------------------------------
vcs :
vcs \
-f files.f -cm line+fsm+tgl+branch+cond \
-timescale=1ns/1ps +vcs+flush+all \
-fsdb -full64 -R +vc +v2k -sverilog -debug_all \
-gui -l vcs_out.log &
#---------------------------------------
verdi :
verdi -f files.f -ssf -sv tb.fsdb &
#---------------------------------
coverage_text :
urg -dir simv.vdb -format text &
#-------------------------------
coverage_html :
urg -dir simv.vdb &
#----------------------------------
cov_verdi :
verdi -cov -covdir simv.vdb &
#----------------------------------------
clean :
rm -rf *~ core csrc simv* vc_hdrs.h ucli.key urg* *.log novas.* *.fsdb* &
#------------------------------------

## Slide 38: Simulation Results on VCS

## Slide 39: Simulation Results on VCS

## Slide 40: Simulation Results on VCS

## Slide 41: Simulation Results on VCS

## Slide 42: Simulation Results on VCS

## Slide 43: Simulation Results on VCS

## Slide 44: Coverage Plan on Verdi

## Slide 45: Coverage Plan on Verdi

## Slide 46: Resources

## Slide 47: Resources
https://edaplayground.com/x/pgqd
https://drive.google.com/drive/folders/1J8qK3HRA0X3-30uCedGeiX85ineHsu5D?usp=sharing

## Slide 48: THANK YOU